## Slide 1: Reusing 60GHz Radios for Mobile Radar Imaging
Yanzi Zhu, Yibo Zhu,
Ben Y. Zhao and Heather Zheng
U.C. Santa Barbara
yanzi@cs.ucsb.edu

## Slide 2: Today and the Future
Today things are controlled by human
  Drones, cars, smartphones, etc.
The future: unmanned autonomous agents
Drone
Delivery/Pickup
Self-driving
Car
Smartphone
Robot

## Slide 3: Today and the Future
Today things are controlled by human
  Drones, cars, smartphones, etc.
The future: unmanned autonomous agents
Drone
Delivery/Pickup
Self-driving
Car
Smartphone Robot
Need Mobile Imaging

## Slide 4: Beyond Localization
Not only “where” (object location), but also “what” (shape and material)

## Slide 5: Requirements
cm-level accuracy
  Mobile (drones ~40cm) and objects (~20cm) are small
  Google self-driving car requires ~3cm
Robust: work in various conditions
  Darkness, rain…
Portable & affordable
Drones at night

## Slide 6: Existing Solutions Not Suitable
Vision- and sound-based
  Not working in darkness, or with background noise
  Cannot tell object material
Traditional radar
  Bulky (>1m, >10kg) and expensive
Modern radar (e.g., mmWave)
  Require specialized hardware

## Slide 7: WiFi Imaging
Fundamentally limited by resolution
radar resolution = wavelength × distance / antenna array size
distance = 3m
smartphone-sized array
(10cm)
resolution = 1.8m

## Slide 8: Leveraging 60GHz Radios
Robust, portable, and affordable (<$37.5)
  Work in darkness and rain[1]
Stable and predictable propagation
  High directionality & minimal multi-path effects
Resolution is 12× better than WiFi 5GHz
resolution = wavelength × distance / array size
Tri-band Wi-Fi solutions from Qualcomm Atheros
integrate … 60 GHz spectrum band along
with … 5 GHz band and … 2.4 GHz band.
-- Qualcomm Press Release
[1] Demystifying 60GHz Outdoor Picocells. MobiCom, 2014

## Slide 9: Synthetic Aperture Radar
Key idea of SAR:
  Emulate a large antenna array using a small antenna
Real array combines measurements from different elements
Synthetic array moves the antenna to receive signal at different locations
1m
1m
TX
TX
∝

## Slide 10: SAR Insufficient
Problem: movement noise > wavelength (5mm)
mm-level localization impossible
Noise causes phase error → poor imaging results
E.g., noise-free vs. 5mm random noise
Ideal
Actual
32cm error!

## Slide 11
SAR
Our Approach
surface = many points
Imaging Result
Object
surface = single unit
RSS Profiles
Location, Material,
Curvature, Width
↑
→
Measurements
Object
Sensitive to movement noise
Robust to movement noise
RSS + Phase
RSS + AoA (60GHz)
TX

## Slide 12
SAR
Our Approach
surface = many points
Imaging Result
Object
surface = single unit
RSS Profiles
Location, Material,
Curvature, Width
↑
→
Measurements
Object
Sensitive to movement noise
Robust to movement noise
RSS + Phase
RSS + AoA (60GHz)
RSS Series Analysis

## Slide 13: System Overview
Sensing objects and movement planning
RSS Series Analysis
TX
Object
Beam on direction 2
Move 1m along this direction
RX
Measurements
1
3
2
location→ curvature → width→ material
RSS Profiles

## Slide 14: Determine Curvature
Principle: surface reflects signals like a mirror
(60GHz) AoAs of strongest RSS → TX mirror point
TX mirror point → curvature and radius
TX
Mirror of TX
Physics + Geometry
Mirror of TX
TX
Object Location

## Slide 15: Determine Width
Principle: RSS shape varies with surface width
Modeling 60GHz reflection → predict RSS profiles
0
1
0
1
30cm
flat
10cm
flat
Norm. RSS
Measurement Index
Measurement Index
Norm. RSS
Predict
30cm
Predict
10cm
⋮
0
1
Norm. RSS
0
1
Norm. RSS
Best match!
Estimated width = 10cm

## Slide 16: Testbed
Ideal: steerable phased array (unavailable)
Our testbed: HXI radios + horn antenna
  Fine-grained mechanical rotator (unit of 0.15°)
  Phased array main beam similar to horn
  EIRP is 17dB weaker than commodity radios[1]
[1] Wilocity’s 60GHz chipset from Qualcomm (whitepaper)

## Slide 17: Experiments with Real Objects
Centimeter accuracy
  Localization error < 10cm
  Width error < 4.5cm
Narrow down to 3 materials among 39 choices in database
TX-object distance = 2m & RX-object distance = 3.5m
Inject <10cm trajectory deviation and positioning error
Curved
Flat

## Slide 18: Only The First Step
Leverage 60GHz radios to image the objects in presence of movement noise
First step towards 3D mapping
  2D is feasible when devices move to cover an area
Limitations
  Focus on static objects
  TX and RX need line-of-sight to the objects
  Lack fine-grained details

## Slide 19: Thanks! Questions?